## Slide 1: RAVEN: Improving Interactive Latency for the Connected Car
HyunJong (Joseph) Lee†, Jason Flinn†, and Basavaraj Tonshal⏀
University of Michigan†, Ford Motor Company⏀

## Slide 2: Vehicles are connected over many networks

## Slide 3: The connected car is a hotspot

## Slide 4: Apps perform poorly in vehicle
Apps in vehicle perform poorly
These apps are latency-sensitive
Wireless networks in vehicle:
  Significant variation in latency
  Extremely unpredictable tail latency

## Slide 5: Uncertainty in prediction for multi-network
RTT
RTT

## Slide 6: Uncertainty in prediction for multi-network
1
2
3
1
2
3
1
2
3
RTT
RTT
Benefit: redundancy reduces latency under uncertainty
Cost: increased resource usage
Strategic redundancy balances benefit & cost

## Slide 7: Overview
  Study of current wireless network connectivity in vehicle
  Design and implementation of RAVEN
    Employs strategic redundancy
  Evaluation
    Emulation
    Live vehicle experiments

## Slide 8: Study of vehicular networking
Measure network RTT of 3 networks simultaneously
Scenarios: downtown, highway, rural area, suburban

## Slide 9: RTT distributions for 3 networks
Different networks have different distributions
Commercial WiFi offers good performance
Tail latency is extremely high for all networks

## Slide 10: RTT variation
Latency variation is high and unpredictable
Given network remains best network is 2 seconds in median

## Slide 11: Study of vehicular networking: summary
Different networks have different distribution
Wireless networks in vehicle exhibit extremely high tail RTT
In short term, RTT is very unpredictable
Uncertain which network offers the best RTT at given time

## Slide 12: Overview
  Study of current wireless network connectivity in vehicle
  Design and implementation of RAVEN
    Employs strategic redundancy
  Evaluation
    Emulation
    Live vehicle experiments

## Slide 13: Solution to multi-networks: MPTCP
Expected latency
Expected latency
1
2
3
4
5
6
7
4
5
6
7
MPTCP missed important opportunity
by not employing redundancy

## Slide 14: Moving expected latency to distribution
RTT
RTT
Expected latency
Expected latency
Expected latency
Expected latency

## Slide 15: Embracing uncertainty
RTT
RTT
RTT
Strategic redundancy
Send redundantly over networks
with confidence intervals overlap
1

## Slide 16: Tunable knob: % of confidence interval
2
2
RTT

## Slide 17: How to estimate RTT with stale samples?
time
Order-based weight does not account for stale samples
Time-based weight accounts for
recency of samples

## Slide 18: Temporarily poor performing network
1
2
3
RTT
RTT

## Slide 19: Replacing active probing with aging
2
RTT
2

## Slide 20: How to identify latency-sensitive traffic?
Problem: should only use redundancy when it matters
Prior systems require apps to disclose size, importance:
  DEMS, Intentional Networking, ...
RAVEN automatically identifies traffic
  Small transfers likely to be RTT-sensitive  redundancy
  Large transfers not impacted much by RTT  implies striping

## Slide 21: In the paper
In kernel implementation of MPTCP scheduler
Cancels work that becomes useless
Details of algorithm

## Slide 22: Overview
  Study of current wireless network connectivity in vehicle
  Design and implementation of RAVEN
    Employs strategic redundancy
  Evaluation
    Emulation
    Live vehicle experiments

## Slide 23: Speech recognition in emulation
Chart: Response time in msec
| 48.768999999999998 | 58.904000000000003 | 58.906999999999996 | 66.941000000000003 | 72.802000000000007 | 75.040000000000006 | 77.031999999999996 | 79.043000000000006 | 80.879000000000005 | 82.673000000000002 | 82.948999999999998 | 84.084999999999994 | 84.885999999999996 | 85.052999999999997 | 86.852000000000004 | 87.061000000000007 | 88.853999999999999 | 90.873999999999995 | 92.87 | 94.977000000000004 | 100.95099999999999 | 234.89699999999999 | 357.03399999999999
Verizon | 0 | 0.05007 | 0.05146 | 0.10014 | 0.15021 | 0.20028 | 0.24896 | 0.30042 | 0.35049 | 0.40056 | 0.45063 | 0.5007 | 0.55076 | 0.60083 | 0.6509 | 0.70097 | 0.75104 | 0.80111 | 0.85118 | 0.90125 | 0.95132 | 0.99861 | 1
Sprint | 0 | 0.05007 | 0.05146 | 0.10014 | 0.15021 | 0.20028 | 0.24896 | 0.30042 | 0.35049 | 0.40056 | 0.45063 | 0.5007 | 0.55076 | 0.60083 | 0.6509 | 0.70097 | 0.75104 | 0.80111 | 0.85118 | 0.90125 | 0.95132 | 0.99861 | 1
XFinityWiFi | 0 | 0.05007 | 0.05146 | 0.10014 | 0.15021 | 0.20028 | 0.24896 | 0.30042 | 0.35049 | 0.40056 | 0.45063 | 0.5007 | 0.55076 | 0.60083 | 0.6509 | 0.70097 | 0.75104 | 0.80111 | 0.85118 | 0.90125 | 0.95132 | 0.99861 | 1
TCP over all networks have high tail latency

## Slide 24: Speech recognition in emulation
RAVEN improves median latency up to 30% over MPTCP
RAVEN reduces tail latency up to 5x over MPTCP
Chart: Response time in msec
| 48.768999999999998 | 58.904000000000003 | 58.906999999999996 | 66.941000000000003 | 72.802000000000007 | 75.040000000000006 | 77.031999999999996 | 79.043000000000006 | 80.879000000000005 | 82.673000000000002 | 82.948999999999998 | 84.084999999999994 | 84.885999999999996 | 85.052999999999997 | 86.852000000000004 | 87.061000000000007 | 88.853999999999999 | 90.873999999999995 | 92.87 | 94.977000000000004 | 100.95099999999999 | 234.89699999999999 | 357.03399999999999
Verizon | 0 | 0.05007 | 0.05146 | 0.10014 | 0.15021 | 0.20028 | 0.24896 | 0.30042 | 0.35049 | 0.40056 | 0.45063 | 0.5007 | 0.55076 | 0.60083 | 0.6509 | 0.70097 | 0.75104 | 0.80111 | 0.85118 | 0.90125 | 0.95132 | 0.99861 | 1
Sprint | 0 | 0.05007 | 0.05146 | 0.10014 | 0.15021 | 0.20028 | 0.24896 | 0.30042 | 0.35049 | 0.40056 | 0.45063 | 0.5007 | 0.55076 | 0.60083 | 0.6509 | 0.70097 | 0.75104 | 0.80111 | 0.85118 | 0.90125 | 0.95132 | 0.99861 | 1
XFinityWiFi | 0 | 0.05007 | 0.05146 | 0.10014 | 0.15021 | 0.20028 | 0.24896 | 0.30042 | 0.35049 | 0.40056 | 0.45063 | 0.5007 | 0.55076 | 0.60083 | 0.6509 | 0.70097 | 0.75104 | 0.80111 | 0.85118 | 0.90125 | 0.95132 | 0.99861 | 1
MPTCP | 0 | 0.05007 | 0.05146 | 0.10014 | 0.15021 | 0.20028 | 0.24896 | 0.30042 | 0.35049 | 0.40056 | 0.45063 | 0.5007 | 0.55076 | 0.60083 | 0.6509 | 0.70097 | 0.75104 | 0.80111 | 0.85118 | 0.90125 | 0.95132 | 0.99861 | 1
RAVEN (90%) | 0 | 0.05007 | 0.05146 | 0.10014 | 0.15021 | 0.20028 | 0.24896 | 0.30042 | 0.35049 | 0.40056 | 0.45063 | 0.5007 | 0.55076 | 0.60083 | 0.6509 | 0.70097 | 0.75104 | 0.80111 | 0.85118 | 0.90125 | 0.95132 | 0.99861 | 1

## Slide 25: Speech recognition in live experiment
RAVEN improves median up to 80% over MPTCP in live
RAVEN reduces tail latency up to 2x over MPTCP in live
Chart: Response time in msec
| 18.207999999999998 | 62.823 | 64.308000000000007 | 65.834000000000003 | 67.076999999999998 | 70.539000000000001 | 74.156000000000006 | 94.352999999999994 | 107.212 | 110.008 | 114.536 | 117.53 | 121.31699999999999 | 124.599 | 127.166 | 130.94900000000001 | 134.62100000000001 | 139.61799999999999 | 148.923 | 289.00599999999997 | 721.125 | 1634.3889999999999
MPTCP | 0 | 0.051873 | 0.10086 | 0.14986 | 0.20173 | 0.25072 | 0.29971 | 0.35158 | 0.40058 | 0.44957 | 0.50144 | 0.55043 | 0.59942 | 0.6513 | 0.70029 | 0.74928 | 0.80115 | 0.85014 | 0.90202 | 0.95101 | 0.99712 | 1
RAVEN (90%) | 0 | 0.051873 | 0.10086 | 0.14986 | 0.20173 | 0.25072 | 0.29971 | 0.35158 | 0.40058 | 0.44957 | 0.50144 | 0.55043 | 0.59942 | 0.6513 | 0.70029 | 0.74928 | 0.80115 | 0.85014 | 0.90202 | 0.95101 | 0.99712 | 1

## Slide 26: Yelp in live experiment
Chart: Response time in msec
| 47.387999999999998 | 137.43199999999999 | 181.65899999999999 | 211.21199999999999 | 267.08499999999998 | 290.839 | 321.54399999999998 | 358.90100000000001 | 413.35899999999998 | 447.19900000000001 | 484.26600000000002 | 537.58799999999997 | 616.35500000000002 | 749.05 | 844.92 | 1042.0170000000001 | 1179.4739999999999 | 1660.2280000000001 | 1759.5360000000001 | 2361.1680000000001 | 3234.6979999999999
MPTCP | 0 | 0.047619 | 0.10714 | 0.15476 | 0.20238 | 0.25 | 0.30952 | 0.34524 | 0.40476 | 0.45238 | 0.5 | 0.54762 | 0.60714 | 0.65476 | 0.70238 | 0.75 | 0.80952 | 0.85714 | 0.90476 | 0.95238 | 1
RAVEN (90%) | 0 | 0.047619 | 0.10714 | 0.15476 | 0.20238 | 0.25 | 0.30952 | 0.34524 | 0.40476 | 0.45238 | 0.5 | 0.54762 | 0.60714 | 0.65476 | 0.70238 | 0.75 | 0.80952 | 0.85714 | 0.90476 | 0.95238 | 1
RAVEN improves median latency by 5x for Yelp in live
MPTCP interacts poorly with power management (PM)
5x

## Slide 27: Effectively identify latency-sensitive traffic
Small transfer, all data are sent redundantly
Large transfer, first a few bytes are sent redundantly
Application | Redundant %
File Download (1K) | 100 %
Web Browsing | 4.90 %
File Download (1M) | 1.27 %
Application Install | 0.59 %
Video Streaming | 0.03 %

## Slide 28: Conclusion
Cars are connected to infrastructure over multiple networks
Apps used in vehicle are latency-sensitive
Wireless networks in vehicle have unpredictable, poor latency
RAVEN is a MPTCP scheduler that employs strategic redundancy to hedge a bet against uncertainty
VNperf & traces available at http://vnperf.github.io